## Slide 1: SDR Radio Astronomy Receiver
Sponsored by: GVSU Physics Department
Design by: Phil Behnke, Dan Soberal, Sean Bredeweg

## Slide 2: What are SDRs?
Analog
Digital
Notes: Phil
Analog Radio
  Fixed Frequency/Bandwidth
  Changes in radio parameters require change in hardware.
  Everything is analog.
Digital Radio
  Get an ADC as close to antenna as possible.
  Can instantaneously use multiple channels
  Modulation, frequency selection, bandwidth are all defined in software using digital signal processing.

## Slide 3: Purpose
Radio Astronomy
  Monitoring RF emissions from space
  Learn about the Universe and about Earth
Radio Jove
  NASA sponsored amateur radio astronomy kit.
  Completely analog (Direct Conversion Receiver)
  Used to listen to Jupiter (20 MHz)
Redesign Radio Jove to use SDR techniques
Notes: Dan

## Slide 4: Requirements
Operate at 20.1 MHz.
Capture a 1 MHz bandwidth.
100 dB dynamic range.
Capture ~1 microvolt signals from Jupiter.
Be able to record data or analyze data on the fly.
Mix signal to audio and send to headphones.
Notes: Sean
Early on when the project was first being discussed, we were given a list of requirements for the receiver. Upon further research, some of the requirements were going to be very difficult to achieve the with hardware that was available.
Some of the
We designed our system to operate at a center frequency of 20.1 MHz
After the FPGA approximately 1MHz bandwidth
We were told that we needed to be able to detect a 1 microvolt signal
  The LNA, filters, and gain stages amplify the what is desired and attenuate everything else to the noise floor
Be able to record data or analyze data on the fly
  To do this we need to transfer the 1 MHz bandwidth in real time to the PC
There are many other requirements that are detailed in the functional specification document. These few listed here are the requirements which greatly influenced the hardware choices in our design.

## Slide 5: System Overview
Notes: Phil

## Slide 6: Receiver Block Diagram
Receiver
PC running custom DSP software
USB 2.0
Audio output to headphones
Signal from antenna
RF Front End
Pre-processing
Audio converter
Knob to control output volume
Knob to control center frequency
Power Switch
Notes: Sean
As was depicted in the high level overview of the system in the last slide, the antenna is connected to the receiver which is connected to the pc. Here we have block diagram of the physical receiver which can be split up into three separate blocks: the RF front end, pr-processing block, and the audio converter.
From the diagram we can see that the antenna signal path enters the RF front end, proceeds to the pre-processing block where the signal is then fed to the PC and the audio converter block.
The RF front end is designed to filter the incoming spectrum and amplify the frequency band of interest. Dan will go into further detail about this particular block.
The pre processing block is designed to digitize analog data, perform digital filtering, and pass the data via USB to the PC. I will be speaking about the analog to digital conversion, Dan will touch on the FPGA and Phill will talk about the USB.
The audio converter block is designed to take a very narrow band of the 1MHz bandwidth, mix with an intermediate frequency to audible range, and then output the audio to a head phone jack. The purpose of this is for verification that the receiver is operating when being initially setup. The volume of the audio and center frequency of the audible signal can be adjusted using tuning nobs on the receiver.

## Slide 7: RF Front End
 |  |  | Stage |  |  | 
Parameter | Pre-Filter | LNA | GAIN 1 | GAIN 2 | Filter (AA) | GAIN 3
Gain (dB) | -4.67 | 16 | 19 | 19 | -15 | 19
NF (dB) | 0.00053 | 3.5 | 4.3 | 4.3 | 0.00053 | 4.3
IP3 (dBm) | Inf | 13 | 13 | 13 | Inf | 13
P1dB (dBm) | Inf | 2.9 | 22 | 22 | Inf | 22
Notes: Dan

## Slide 8: Noise Analysis
 |  |  | Stage |  | 
Parameter | Filter | LNA | GAIN 1 | GAIN 2 | MIXER
Gain (dB) | -5 | 16 | 19 | 19 | 17
NF (dB) | 0.00053 | 3.5 | 4.3 | 4.3 | 5

## Slide 9: Dynamic Range
 |  |  | Stage |  | 
Parameter | Filter | LNA | GAIN 1 | GAIN 2 | MIXER
Gain (dB) | -5 | 16 | 19 | 19 | 17
IP3 (dBm) | Inf | 13 | 13 | 13 | -13
P1dB (dBm) | Inf | 2.9 | 22 | 22 | NA

## Slide 10: Component Selection
Integrated Circuits
  LNA = MAX2611, RF Gain = RF2312, Mixer = SA612
Passive Components
  Inductors and Capacitors
    SRF far away from operating frequency
    High Q, Low ESR
  Resistors
    Thermal Noise

## Slide 11: Pre-Filtering
3rd Order Filter Chebyshev Filter
Shunted endpoints
Passband (-3 dB down) = 18 MHz – 22 MHz
Bandwidth is approximately 4 MHz
Attenuation at 15 MHz: 37.8 dB
Attenuation at 25 MHz: 30.1 dB
Notes: Dan

## Slide 12: Anti-Aliasing Filtering
4th Order Butterworth Filter
Mesh capacitor coupled
Passband: 19.4 MHz to 20.6 MHz
Attenuation at 15 MHz: 80.0 dB
Attenuation at 25 MHz: 89.2 dB
Notes: Dan

## Slide 13: RF FRONT END RESULTS
Low Noise Amplifier Stages: 1
Gain Stages: 3
Filters: 2
Total Gain = 53.3 dB
Minimum Discernable Signal = 107 dBm
NF = 3.5828 dB
Noise Floor = 107.417 dBm
Dynamic Range = 88.9 dB
System Attenuation at 25 MHz : 119.3 dB
System Attenuation at 15 MHz: 117.8 dB

## Slide 14: Analog to Digital Conversion
ADC
RF front end
FPGA
LVDS
to
CMOS
ADC Clock
ADC Driver
Notes: Alright, after the RF front end adds gain to the frequency band of interest and attenuates everything outside to the noise floor, the next step is to digitize the data and then send it to the FPGA for analysis.
The ADC is the hardware that bridges the gap between the analog and digital realm. There are several other pieces of hardware that are necessary for the ADC to operate at its peek performance. These include an analog input driver, a high quality clock source, and in our case a LVDS to LVCMOS line driver.
In the next few slides we will take a very brief look at each of these pieces of hardware, as well as the ADC.

## Slide 15: Analog to Digital Conversion
ADC Driver – AD8352
  Ultra low distortion, low noise RF amplifier
  Adjustable common mode
  Adjustable gain up to 20dB
  Low power
  High OIP3 value
  Buffered gain setting resister
  Convert single ended to differential ended
Notes: Low noise input stage, 2.7nV per root Hz at a gain of 20dB

## Slide 16: Analog to Digital Conversion
ADC Clock Synthesizer –AD9573
  100 MHz output when supplied with 25MHz
  0.54 ps RMS jitter
  Includes a loop filter and regulator for supply noise immunity
  Differential output
  LVDS/LVCMOS output
  Maximum voltage swing of 6.0Vp-p
Notes: Simple design which requires a 25 MHz input signal and outputs a stable 100MHz signal with 0.54 ps RMS jitter
The ADC requires a differential clock source. It is recommended that the voltage swing not be full scale CMOS as the large voltage swings may induce noise in the ADC.
The synthesizer’s LVDS/LVCMOS output is ideal for the for the clock lines of the ADC.

## Slide 17: Analog to Digital Conversion
ADC – AD9460
  105 MSPS
  78.1 dB SNR
  88 dB SFDR
  Excellent linearity
  LVDS and CMOS compatible
  2.0Vp-p to 4.0Vp-p Input
  12.7 ENOB
  0.06 ps internal jitter
Notes: We are selecting the 2.0Vp-p input, and the LVDS outputs of the ADC. This is because dynamic performance, including SNR and SFDR, are maximize when LVDS mode is selected.
With an effective number of bit of 12.7, we can expect the actual resolution of the ADC to 300.57 µV between each quantivation level.

## Slide 18: Analog to Digital Conversion
Notes: Analog devices has a simulation tool that has allowed us see the expected performance of the our particular ADC. Inputting the actual performance specifications, 100MSPS, 0.6 ps rms jitter, 20.1 MHz fundamental frequency, and amplitude relative to the ADC’s full scale capability. Using this tool we can get an idea of the ADC’s actual performance in regards to SNR, SFDR, and distortion.
Performance is also influenced by the quality of components used and the layout of these components. Special care must be taken in the layout of the ADC and its supporting hardware in order for its correct operation.
We have purchased a development board for this ADC directly from analog devices.

## Slide 19: FPGA
19 MHz

## Slide 20: Data to the PC
  USB
  Ethernet
  Firewire
  Sound Card
Notes: A USB 2.0 connection will be used to send data from the receiver to the PC.
USB 2.0 has a theoretical maximum speed of 480 Mbps.
USB is ubiquitous.
USB in isochronous mode.
  Used for streaming data.
  Guaranteed data rate.
  No error correction.

## Slide 21: USB
Cypress FX2LP (CY7C68013)
Notes: Cypress FX2LP USB transceiver.
  CY7C68013
  Integrated 8051 microcontroller.
    Sets up USB interface and “gets out of the way”
    Can compile firmware using Small Device C Compiler (SDCC)
  Capable of High-Speed (480Mbps)
  Four 16 bit FIFO buffers.
  Capable of isochronous mode.
  No non-volatile memory
    Will download code from PC in a process called ReNumeration.

## Slide 22: USB Speed
19 MHz

## Slide 24: PC
LibUSB
  Userland driver!
  Supports both bulk isochronous mode.
  Used by the USRP of GNU Radio
  Several Python wrappers available.
    Can go straight from LibUSB to GNU Radio.

## Slide 25: PC

## Slide 26: Software Requirements
Real Time Mode | Radio Astronomy Mode | Full Record Mode | Data Analysis Mode
Process to audio | Plot integrated RMS average of live signal energy over entire bandwidth | Save unprocessed data as WAV file. | Process WAV file using Radio Astronomy Mode.
Optionally save audio stream | Export in CSV format. | Display waterfall. | 
Waterfall plot |  |  | 
Notes: The PC will perform most of the digital signal processing.
  FFT
  Waterfall plot
  Audio processing
Two Linux USB drivers will be used.
  Identify the FX2 and download the correct firmware.
  Get the data off the bus.
Second driver will get data off the bus and send it to a TCP socket.

## Slide 27: User Application
GNU Radio Backend
Python Frontend

## Slide 28: GNU Radio

## Slide 31: Budget
Front End Components (resistors, capacitors, inductors, connectors, etc): $95
Analog to Digital Converter: $114
FPGA (Nexys II Board): $100
Cypress FX2LP: $17
TOTAL: $326
Notes: Sean

## Slide 32: Timeline